## Slide 1
Excalibur architecture: high-speed IP services to home PCs
Mario P. Vecchi
Excalibur Group
A Time Warner Company
mario.vecchi@excalibur-group.com
IP Applications
Over Cable Network (IPACD) BOF
IETF Montreal, June 24, 1996
(Anonymous ftp at twcable.com:/pub/EXCALIBUR/*)

## Slide 2
General Service Properties
Connectionless access: LAN-like service, no dial-up, permanently connected, automatic “BW-on-demand”.
High speed: 8-25 Mb/s downstream, 1-3 Mb/s upstream, shared BW.
Standard datacom: mainstream Internet technology (TCP/UDP/IP), leverage new multimedia extensions (IPng).
Client-server infrastructure: enabling TWC environment, evolve to new services.

## Slide 3
What is Excalibur’s model?
Excalibur is an enabling networking and distributed computing environment.
Deliver LineRunnerTM information services.
Multivendor end-to-end solution, based on IP internetworking and related applications => open, extensible and manageable.
Supports high-speed multimedia interactive PC applications - it is NOT an entertainment video environment.
Leverages TWC’s broadband HFC access network, and metropolitan fiber networks, to create regional broadband IP infrastructure (“intranet”).
Provides local and national services - and content - focused on residential customers, with national and global IP connectivity (Internet and “internets”)

## Slide 4
How is Excalibur structured?
Networking:
  Access network: HFC broadband and cablemodems (Ethernet).
  Metropolitan fiber broadband backbone (ATM/ SONET, FDDI...)
  Global access: Internet, on-line services, enterprises, NOC, ...
Client SW:
  Browser, e-mail, usenet, telnet, ftp...
  Install, log-in, account mgmt, SW download...
Server SW:
  Subscriber Mgmt, Session Mgmt, Content Mgmt, http, SMTP, NNTP, DNS, DHCP...
  Network Mgmt, System Admin, Billing, Events Logging, Security and Firewalls...

## Slide 5
Excalibur Global View
SONET
Analog
Digital
entertainment
Distr.
Hub
Distr.
Hub
Distr.
Hub
Distr.
Hub
Primary
Headend
300,000hp
Fiber
Node
500hp
Distr.
Hub
20,000hp
Distr.
Hub
HFC and
Backbone
Homes
Enterprises and Local Content
TimeWarner
Cable Systems
IXCs, National IP
Interconnection
Internet
PSTN
OLSPs
LineRunnerTM
National
Content
NOC,
Help Desk
SONET
Analog
Digital
entertainment
Distr.
Hub
Distr.
Hub
Distr.
Hub
Distr.
Hub
Primary
Headend
300,000hp
Fiber
Node
500hp
Distr.
Hub
20,000hp
Distr.
Hub
OLSPs
PathfinderTM
Schools
Business

## Slide 6
Typical TWC Division Layout
SONET
Analog
Digital
entertainment
Distr.
Hub
Distr.
Hub
Distr.
Hub
Distr.
Hub
Primary
Headend
300,000hp
~ 30 mi
~ 10 mi
Fiber
Node
500hp
Distr.
Hub
20,000hp
Distr.
Hub

## Slide 7
Excalibur Reference Architecture
Headend
Distr. Hubs
RF
RF
25Mb/s
1-3Mb/s
Signal
Conversion
System
IP switch
router
OC3/DS3, FDDI
Internet
Enterprises
NM/OSS
Servers
Gateway
Router
Appl. Level
Gateway
NOC,
Help desk
On-line
services
Billing
system
Remote
dial-in
Local
Content
500 homes
300,000 homes
20,000 homes
Fiber
Nodes
National
Content
Cablemodem
10baseT
Ethernet
Fiber
Coax

## Slide 8
HFC Spectrum Usage
POTS
LineRunner,
1-2 MHz
Set-tops
Reverse
Spectrum
Forward
Spectrum
LineRunner,
6MHz channel(s)
550-750 MHz
40MHz
6 MHz
6 MHz
40MHz
. . .
I-TV
Reverse
Spectrum
I-TV

## Slide 9
Cablemodem
Self-installing and adaptive: key operational requirements for large-scale deployment.
Asymmetrical, yes, but high-speed both ways:
  64QAM, 24 Mb/s in 6 MHz down (QPSK initially?)
  QPSK, 1-3 Mb/s in 1-2 MHz up
Ethernet 10baseT to PC:
  Multiple PCs in the home/small business.
  Filter network traffic on MAC address.
Vendor-specific MAC protocol, future standard.
TW part of industry effort to define interoperable cablemodem.
Link-level encryption required over HFC.

## Slide 10
Signal Conversion System
SCS at the Distribution Hub, aggregates traffic from about 20,000 hp (40 fiber nodes):
- Terminate cablemodems: physical and link levels.
- Connect to Headend router: deliver IP datagrams (over ATM/SONET, FDDI, ...).
Decouple up streams from down streams, scale from low-penetration:
  Forward: start one mod for all users, install additional cards as needed.
  Reverse: RF clusters of fiber nodes, add additional demods as needed.
Support multicasting/broadcasting.

## Slide 11
Illustrative example: SCS Modular Growth
Hub
(IP/ATM)
to
Headend
MAC
control
64QAM
25 Mb/s
QPSK 1
3 Mb/s
QPSK 8
3 Mb/s
combine
traffic
RF
mix
RF
mix
Rx1
Rx5
Rx35
RxN
to
Fiber
Nodes
from
Fiber
Nodes
RF
split
Tx1
Tx2
TxN
SCS at DH

## Slide 12
LineRunnerTM Applications
Client SW on customer’s PC: open IP apps.
Broadband multimedia environment, html/http extending to Java, vrml, etc..
Compelling GUI, launch other apps.
Three levels of apps for LineRunnerTM:
  Basic: browser, email, ftp, telnet. Content: national and local, newspapers, schools, business, government, weather, sports, etc.
  Enhanced: add unrestricted Internet access.
  Premium: all other third-party (OLSP, work-at-home, shopping, etc.)
User tools: install, login/logout, account/subaccount management, network download, etc.

## Slide 13
LineRunnerTM account management
Login validates account and cablemodem:
  Activate link-level encryption.
  Assign IP addreses (DHCP), enable TCP/IP stack.
Master account holder, multiple subaccounts:
  Manage subaccounts, passwords, access levels, etc.
  “Parental control” features.
Enable user mobility, “guest” subaccount type.

## Slide 14
LineRunnerTM Basic services
LineRunnerTM information services:
  Local news, weather, sports, bulletins, etc.
Global Internet email service:
  SMTP gateway, email client using POP protocol.
Launchers for third-party applications (OLSPs, enterprise connection, schools, games, etc.)
Selectively authorized URLs for LineRunnerTM basic customers.

## Slide 15
Access to OLSP
Provide launching from LineRunnerTM interface.
Each OLSP deals directly with customers, for both client software and account/billing.
OLSP can have local servers at Headend, outside our firewall.
Connect through gateway/IP filtering.
NM information shared across subnetworks, as feasible.

## Slide 16
Access to Internet
“Access to Internet” has multiple functions.
For users: the Internet is an open, global information service.
User will have LineRunnerTM client apps (or theirs):
  Our TCP/IP stack, when needed.
  Browser in open mode.
  telnet, ftp, gopher, whois, finger, etc.
Access to any site on worldwide Internet. Restricted access from the outside to our servers and clients.
(cont.)

## Slide 17
Access to Internet (cont.)
For system: the Internet is a global network to find and carry information,when appropriate.
Some LineRunnerTM content may be distributed using the Internet.
Other premium www sites will be accessed over the Internet.
New services and applications as well: electronic commerce, MBONE, I-phone, etc.

## Slide 18
Remote dial-in access
Provide phone access toLineRunnerTM service.
Low-speed (28kb/s) or ISDN access for traveling customers, and for homes beyond cable franchise.
Aggregate PSTN calls at terminal server, provide TCP/IP traffic to Excalibur edge router.
Client SW first provides login to PPP, then user is presented to usual toLineRunnerTM login process.

## Slide 19
Security capabilities
Link level: encryption over HFC: RSA plus DES, or similar.
Network level: application gateways plus IP filtering:
Session level, for some client applications:
  Kerberos?
  User login with paswords.
Logging and audits to monitor any attacks.

## Slide 20
Enterprise connectivity
A class of third-party premium information services:
  Launched from LineRunnerTM basic interface.
  Provided and billed separately.
Important service for business, academic and governmental campuses:
  Work at home, telecommuting.
  CSCW including residential customers.
  Education, K-12 to universities.
  Remote medicine, patient-doctor consultation.

## Slide 21
Other evolving services
Excalibur is an enabling platform, many new apps will be supported:
  Virtual CD-ROM.
  Interactive, multiuser games.
  Home shopping.
  etc.
Some key technologies for future:
Multimedia apps (Java, Macromedia,...)
Secure NFS services.
Real-time RSVP enhancements.
Electronic commerce protocols.

## Slide 22
Operations support services
Subscription management and billing: interface to existing cable systems.
“It’s another cable product” paradigm.
Generate work order and trigger LineRunnerTM system configuration.
Usage monitoring and event logging:
  Collect sessions information, not packet traffic.
  Log premium services sessions.

## Slide 23
System administration
System Administration (UNIX, NT): key aspect for success of business.
Manage: e-mail, www, DNS, DHCP, IP filtering, appl. gateway, file storage, etc.
Local staff to cover routine tasks and respond to hard failures.
Remote administration, complement local expertise.

## Slide 24
Network management services
Use SNMP standard platforms to build NM applications.
Element Managers for all key components:
  At Headend: servers, switches, routers.
  At DH: SCS, routers.
  At home: cablemodem, user PC?
Provide single point of entry for NM operator, integrated solution for multivendor roll-out.
Cablemodem and SCS must support TWC’s csmi MIB (Spectrum Management Application).

## Slide 25
Customer support services
Provide complete coverage of user’s requests over single 800-number access.
Resolve all issues regarding client apps, account management, cablemodem, LAN card.
Remote, centralized customer support, coverage 12x7 minimum, 24x7 preferable.
Local staff for network plant and hard failures only.

## Slide 26
Content management
LineRunnerTM national content created in NYC, distributed to regional systems.
Local content creation: customizing and branding from basic content templates.
Heavy use of html/http technology.Caching http servers.
Third-party services and applications responsible for their content and local servers.

## Slide 27
Elmira, NY trial (Southern Tier On-Line Community)
Market test of LineRunnerTM concept: content, operations, customer support, etc.
Started early June ‘95, it has 250 users:
  about 75 free to community (schools, libraries, etc.)
  about 175 paying customers: $14.95/mo Basic, $9.95/mo Enhanced, no time or usage charges.
Client-server system, (almost) full LineRunnerTM functionality: Hewlett-Packard implementation.
Cablemodem: interim product for trial, Zenith Homeworks, 4 Mb/s symmetric.
Binghamton/Elmira/Corning will be a 1996 commercial deployment, conclude Elmira test phase.

## Slide 28
Elmira trial

## Slide 29
Commercial Deployment Plans
LineRunnerTM commercial deployment in several metropolitan systems in 1996.
TW Cable continues multibillion investment to upgrade HFC plant for 11+ million homes.
Over past 2 years developed multivendor end-to-end solutions, built to Excalibur specs:
  Hewlett-Packard (Cisco, Netscape, Cabletron...)
  Toshiba (Sun, Cisco, Netscape...)
  Cablemodem purchases from Motorola and Toshiba.
  Client SW collaboration agreement with Microsoft.
Other deployment/vendor announcements to follow.