## Slide 1
Round-trip Delay: An exercise in defining an Analytical Metric
Guy Almes and Jamshid Mahdavi
Montreal IETF
25 June 1996

## Slide 2
Overview
Singleton Metric
  Simple version
  Less simple version
  Several different methods
Sampling
Statistics

## Slide 3
Singleton Metric for Round-trip Delay
Idea: zero-length IP packet round trip
Format:
  Name
  Parameters
  Units
  Definition
  A-frame required
  Methodology/ies

## Slide 4
Simple Version
Name: Round-trip delay between two hosts
Parameters: hosts H1, H2, time T (, and implicitly the current round-trip route between H1 and H2)
Units: seconds
Definition: The time it takes to send a zero-length packet from H1 to H2, plus the time it takes to send a zero-length packet from H2 to H1

## Slide 5
Simple Version, continued
Methodologies:
  [1] Send an ICMP Echo Request, time until the return ICMP Echo Reply is received. Use smallest possible IP packet (28 bytes).
  [2] Send an IP packet with LSRR option (via H2, go to H1). Use smallest possible IP packet.
  [3] Do either of [1] or [2] with two different packet sizes P1 and P2, with P2 = 2*P1, resulting in measurements RT1 and RT2. Estimate delay using the formula 2*RT1-RT2.
  [4] Do [3] with several different packet sizes and extrapolate.

## Slide 6
Less Simple Version
Name, Parameters, and Units: the same
Definition: Define
  Link: with properties propagation delay (and transmission rate)
  Router and Host: with properties processing time and queueing time
We measure the end-to-end delay, then ascribe components of delay to each of these properties for each host, router, or link along the path.

## Slide 7
Less Simple Version, continued
Methods: the same
In discussion, it seemed that both versions defined the same metric, and that the differences centered on the work taken on in the second version to model all the Internet components along the path. This might be worth doing for a number of reasons, but it does not contribute to the definition.

## Slide 8
Less Simple Version, continued
Examples of possible benefits of developing A-frame terms more completely:
  helps reason about spatial composition
  allows verification of models and simulators
  helps understanding when you can measure some parameters but not others

## Slide 9
Sampling
We often need to measure a singleton metrics a number of times
Such a sampling is parameterized by:
  the number of singleton tests, and the time between them
Examples:
  100 tests spread over a day
  100 tests back to back
  100 tests spread just enough to avoid self-interference
  with randomized times to avoid phase effects

## Slide 10
Statistics
We often need to take statistics of samples. Among those are:
  average (arithmetic or geometric mean)
  minimum or maximum
  percentile
  standard deviation
  posit a form of the distribution, take enough samples to confirm (up to some confidence level) that the distribution is plausable, then report certain parameters of that distribution

## Slide 11
Bulk Transfer Capacity: An Empirically-specifed Metric
Name: Bulk Transfer Capacity
Parameters: hosts H1, H2, time T (, and implicitly the current round-trip route between H1 and H2)
Units: bits/sec
Definition: Expected performance of one state-of-the-art TCP connection
Methodology: run treno