## Slide 1
Subnet Bandwidth Manager: Admission Control over Ethernet
Raj Yavatkar, Intel
Don Hoffman, Sun
Ema Patki, Intel
Notes: 1

## Slide 2
Goals
Step-by-step mapping of int-serv capabilities over Ethernet infrastructure
  short-term solution should work with existing bridges, hubs/switches
  work with IEEE 802.1? for Level-2 support
  ex. traffic flow separation
Step I -- admission control for RSVP traffic and policing at end systems
Step II -- traffic flow separation at hubs/switches
Step III -- traffic control support in hubs/switches

## Slide 3
Objectives for Step I
administrative control over max amount of multimedia traffic over any LAN segment
Rely on end-system policing and rate-adaptive applications for best effort traffic
  slow start type congestion avoidance
Leverage existing RSVP-signaling as much as possible

## Slide 4
Outline
Only architectural discussion
  variations from RSVP message processing rules included
  protocol details, packet formats, etc. NOT included
Discuss possible alternatives

## Slide 5
Overview
SBM (Subnet Bandwidth Manager) responsible for admission control
a designated SBM (DSBM) for each LAN segment
  an SBM may act as DSBM for many segments
SBM is a UDP-based server
soft state in SBM with refresh ala RSVP
  recovery from SBM restart and failures
dynamic binding between SBM and end-systems
  IP multicast based

## Slide 6
Overview (contd.)
At the start, an RSVP node discovers and binds to its DSBM using IP multicast-based protocol
PATH messages sent/forwarded to the session address (NO CHANGE)
Outgoing RESERVE over Ethernet interface unicast to DSBM
  a new LAN_PHOP object specifies the PHOP
DSBM performs admission control and forwards RESERVE toward PHOP

## Slide 7
Overview (contd.)
DSBM processing similar to conventional RSVP processing
  merges reservations appropriately
  avoids killer reservations
  returns RESV_ERROR or RESV_CONFIRM (if necessary)

## Slide 8
LAN
SBM
PATH
Sess.
RESV
RESV
Receiver
Router

## Slide 9
Important Notes
NOT a centralized scheme
Many SBMs can exist per LAN, each responsible for a separate portion of the LAN
Does NOT require maintenance of consistent, distributed state across Hosts and SBMs
Distribution of responsibility among SBMs allows scalability and fault tolerance

## Slide 10
An Alternative Proposal
Assume one SBM per IP subnet
PATH message sent to special SBM address
  mcast to SBM group address (a new encapsulation)
SBM inserts itself as a PHOP between sender and receiver
RESERVE automatically lands up at the SBM
Presented to IEEE 801.P
  does not allow for multiple SBMs within a subnet
  an SBM per hub/switch should be allowed

## Slide 11
Supporting Mechanisms
Discovering DSBM and binding to it
  DSBM listens to a well-known UDP mcast address
DSBM Election
  more than one active SBM for same segment(s)
  single SBM is a DSBM at any time, elected using an election protocol
  Use of I_AM_DSBM declarations via IP multicast and some tiebreaking
  peers step in when DSBM fails or terminates

## Slide 12
Application Behavior
Sender on a LAN not to transmit any traffic until at least one successful RESERVE reaches it
Outgoing flow to be policed to be within maximum RESERVE made
For multicast flows, receivers must leave the session mcast group in case of RESV_ERR or PATH_TEAR
  problematic in case of multiple senders
Best-effort traffic must be rate-adaptive

## Slide 13
Handling Complex Physical Topologies
Multi-hop topology consisting of bridges, hubs, and switches
  data flows traverse only a subset of segments
  multiple DSBMs, each for separate portion of LAN desirable
How to discover topology information?
How to discover peer DSBMs and communicate with them?

## Slide 14
Discovering LAN Topology
techniques used by network management utilities
  static configuration info works only in case of non-redundant paths
an interface to spanning tree topology info needed
  IEEE 802.1 area
IETF hub MIB working group
  topology mapping section

## Slide 15
Topology Discovery Protocol
Placing two endpoints on a map and identifying LAN segments between them
  endpoints identified using MAC addresses
  tell managed hubs in the collision domain to watch for packets with the endpoint MAC address
  send a PING to the endpoint to get it to transmit
  SBM then uses hub MIB interface to read the group/port of target MAC address from managed hubs
  SBM then identifies affected segments

## Slide 17
Host
Host
SBM
R
X
C
B
A
Hub
h1
h2
h3
L3
L2
L1
L4

## Slide 18
Peer-to-Peer DSBM Communication
Peers discovered using SBM_QUERY to SBM_GRP address
  information is cached with time-out
After successful admission control, DSBM forwards a RESERVE to the peer on next hop towards LAN_PHOP
An error is sent back hop-by-hop using reservation state in intermediate DSBMs

## Slide 19
Areas of Co-operation With IEEE 801.P
definition of a standard interface for accessing spanning tree (routing) information in MAUs
mechanisms for traffic flow separation
  ex. priority mechanism
RSVP-based admission control combined with traffic flow separation
  a good approximation to Controlled Load?