## Slide 1
MPOA Update
Defined Mandatory Behavior for Edge Device
  EDFG must recognize flows based on destination
  ICFG & RSFG may recognize flows
Eliminated Proxy Registration of hosts behind edge devices
Simplified, Revised, and Clarified EDFG behavior
  Established a clear demarcation between bridging and routing
Defining Extension to NHRP

## Slide 2
NHRP Extensions
Extending NHRP to deal with Edge devices
At Ingress Edge Device can/must Initiate Query
Defined a semantics of a Trigger to allow a route server to request an Edge Device initiate a shortcut

## Slide 3
NHRP for Egress Edge Device
Defined semantics of a cache imposition protocol
  Allows Route Server to notify ED to expect flow and establish the encaps
Adopted Flow TAGs
  Solves a technical problem on exit cache conflicts
  Allows optimization of exit processing for EDFG
  Defined a format for Tags and an encapsulation for carrying them in data frames