## Slide 1
PktWay Proposed Security Extensions
IETF PktWay (MsgWay) WG
June 24, 1996
Robert T. George
Mississippi State University

## Slide 2
Secure PktWay Team
Work sponsored by the DARPA Secure Heterogeneous Application Runtime Environment (SHARE*HPSC) project
Sanders (Prime contractor):
  Jeff Smith, Fred Shirley, Phil Morano
Mississippi State University (Sub-contractor)
  Anthony Skjellum, Robert George, Thom McMahon
MCNC (Sub-contractor)
  Greg Byrd
Myricom (Secure PktWay architecture design)
  Danny Cohen

## Slide 3
Secure PktWay Goals
Provide secure PktWay communication between trusted SAN’s
  Route data across untrusted SAN’s
Make minimal, non-intrusive changes to PktWay

## Slide 4
Secure PktWay Routing
Packets from a red (trusted) SAN are encrypted and encapsulated into black PktWay ODB’s
  Relies on PktWay L3 forwarding
L2 forwarding is not allowed
  Routing information internal to red SAN’s must not be exposed to black SAN’s

## Slide 5
Secure PktWay Architecture
Red/Black SAN’s:
HR
RED
SAN
RED
SAN
BLACK
SAN
HR
HR
HR

## Slide 6
Secure PktWay Router
Red/Black HR:
Black
HR
Red
HR
Key
Tables
Crypto

## Slide 7
Proposed PktWay Security Extensions (I)
Additional Secure Packet Type
Additional Optional Headers for each Encryption Method
Additional SCID (Security Context ID) Symbol

## Slide 8
Proposed PktWay Security Extensions (II)
Two additional RRP message types
Additional RRP record for authentication
Additional Node Capability for encryption
Two Additional error messages

## Slide 9
Secure PktWay Packet Type
Secure Packet Type:
  Currently proposed as Code 10
  Type Extension Field contains key index
Indicates that PktWay packet contains encrypted ODB
Requires Optional Header

## Slide 10
Secure PktWay Optional Headers
Optional Header for PT = Secure
Contains parameters necessary for data encryption/decryption
Encryption parameters are dependent on encryption method

## Slide 11
Example: SHARE Optional Header
SHARE uses DES
  Optional Header contains long-cycle chaining information
  Initial Value (IV) is 64-bits

## Slide 12
Secure PktWay SCID Symbol
Symbol address undefined, pending PktWay symbol definitions
  Used to designate a negotiated security context between two SAN’s

## Slide 13
Secure PktWay RRP Message Types
SCID RRP Message Type
  Negotiates Security Context with another router
  Currently proposed as Code 11
MLS? RRP Message Type
  Query native security levels from another router
  Currently proposed as Code 12

## Slide 14
Secure PktWay RRP Record
AUTH RRP Record
  Provides a mechanism for authentication of RRP messages
  May be useful for ordinary PktWay

## Slide 15
Secure PktWay Node Capabilities
Secure Node Capability
  Node is capable of handling Secure PktWay packets
  Currently proposed as Code 10

## Slide 16
Secure PktWay Error Messages
PRIVILEGE Error Message
  Indicates insufficient privilege for operation
SECURITY Error Message
  Indicates incorrect security level
KEY Error Message
  Indicates unrecognized encryption key

## Slide 17
Secure PktWay Status
Currently being implemented as a variant of MSU’s UDP PktWay implementation
Implemented as level-C PktWay
  Requires Node Capabilities

## Slide 18
Unresolved Issues
Relationship with PktWay
  Additional fields, separate document, RFC?
Key management
Dynamic discovery