## Slide 1
Tentative MSU PacketWay Multicast Strawman Document Presentation
IETF PktWay (MsgWay) WG
June 24, 1996
Thomas P. McMahon

## Slide 2
Overview
The Multicast Agent
Additional RRP messages
Rules for Multicasting
  for Nodes
  for Half Routers
Implementation Ideas
  Physical layer mapping
  Use of Symbols
  SAN sequence numbers

## Slide 3
The Multicast Agent (MCA)
Each SAN that wishes to provide multicasting for its nodes has one and only one Multicast Agent
A singe Multicast Agent provides a single entry/exit point for multicast messages
The Multicast Agent ensures that all multicast messages ...
  coming into the SAN get sent to all Half Routers of the SAN and to all nodes listening for those messages
  going out of the SAN get sent to all Half Routers of the SAN

## Slide 4
JMCG Addition to RRP
JMCG -- Join Multicast Group
  Sent to a Half Router by node
  Reply is an RDRC RRP message saying which node is the Multicast Agent
  Format....
PktWay Trailer
“JMCG”
“RRP”
ADDR
00
P
Destination-Address
0
0
Data-Length=1
0
0
Source-Address
Logical-Address
PL=0
RL=1
AT=1
1010

## Slide 5
LMCG Addition to RRP
LMCG -- Leave Multicast Group
  Sent to a Multicast Agent by node
  Reply is ????
  Format....
PktWay Trailer
“LMCG”
“RRP”
ADDR
00
P
Destination-Address
0
0
Data-Length=1
0
0
Source-Address
Logical-Address
PL=0
RL=1
AT=1
1010

## Slide 6
Rules for Multicasting
Nodes
  Must insure that all messages sent to a logical address get to the Multicast Agent
  This can be done directly (point-to-point) or via some physical layer multicast/broadcast
Half Routers
  Multicast messages coming into SAN must at least be sent to the Multicast Agent
  Multicast messages going out of the SAN must be sent to the twin HR only

## Slide 7
Possible Implementation for Nodes
ethernet
  similar to what IP does (RFC 1112)
  map the logical address space to ethernet address space
  PktWay multicast is then ethernet multicast
  Multicast Agent subscribes to all multicast groups
RACEway
  can use broadcast or point-to-point
ATM
  must use point-to-point

## Slide 8
Example (outbound)
JMCG
JMCG
JMCG
MA
MA
MA
LA
HR
HR
HR
HR
HR
HR
MA
HR
HR
RDRC MA
RDRC MA
RDRC MA

## Slide 9
Example (inbound)
MA
MA
HR
HR
HR
HR
MA
HR
HR
LA
LA
LA
BROADCAST

## Slide 10
Use of PW (maybe) Symbols
MCA
0
1
3
2
4
5
6
8
9
7
S: FT 6-9
S: FT 1-4
S: FT 3-4
S: FT 8-9
S: FT 6-9 == This is a symbol, Forward this message To addresses 6 - 9

## Slide 11
Potential Duplication Problem
If there is more than one set of intervening SANs between SAN A and SAN Z...
  multiple duplicate Multicast messages will arrive at SAN Z
  FIX: MCA can attach to every Multicast message a SAN ID and SAN sequence number
  Each MCA, as single entry point to SAN, keeps a table of last sequence number received from each SAN
  This can be used by the MCA to eliminate duplicate Multicast messages upon entry to SAN